## Slide 1: Fine-grained Evaluation of Arrival Operations SIDs 2020 2020-12-07
Henrik Hardell Tatiana Polishchuk Lucie Smetanová

## Slide 2: Introduction
Improving ATM efficiency is high on the agenda of aviation policy makers
Key Performance Indicators (KPIs) for objective evaluation
Adaptive KPIs, taking reality into account
Study the effects of different factors in isolated scenarios
Pinpoint inefficiencies
Adoption and enhancement of methodology proposed by EUROCONTROL EC
Data-driven analysis to explore the dynamics of the KPIs
2
Notes: a new project description

## Slide 3: Selected KPIs
Minimum time to final
The minimum time it takes the aircraft to get from its current position to the final point
TMA represented by a square grid
Calculated for each cell of the grid
3
Notes: a new project description

## Slide 4: Selected KPIs
Spacing deviation
Defined for a pair of aircraft and the spacing between them at time t
The difference between the respective minimum times to final
Captures the aircraft’s mutual position in time
4
Notes: a new project description

## Slide 5: Selected KPIs
Sequence pressure
The number of aircraft sharing the same minimum time to final in a given time window
An indicator for measuring the aircraft density in the sequence pressure
5
Notes: a new project description

## Slide 6: Dataset
OpenSky Networks historical database
Opensky data allows exact determination of when aircraft enters TMA and when it reaches the final approach
Data is cleaned, smoothed and filtered, leaving only complete trajectories, from TMA entry to landing
Access to data for all aircraft arrivals to Stockholm Arlanda airport for the year 2018
We use subsets of the data corresponding to different time periods in 2018
6
Notes: a new project description

## Slide 7: Evaluation and data analysis
Use-case scenarios considered:
  Night-time vs daytime operation
  Scenarios with different traffic intensity
  Scenario with heavy delays
  Detecting the hotspots with potential separation violations
7
Notes: a new project description

## Slide 8: Night-time vs daytime operations
    Minimum time to final
Daytime
Night-time
8
Notes: a new project description

## Slide 9: Night-time vs daytime operations
    Spacing deviation
Daytime
Night-time
8
Notes: a new project description

## Slide 10: Night-time vs daytime operations
    Sequence pressure
Daytime
Night-time
9
Notes: a new project description

## Slide 11: Scenarios with different traffic intensity
    Minimum time to final
High-traffic hour
Low-traffic hour
10
Notes: a new project description

## Slide 12: Scenarios with different traffic intensity
    Spacing deviation
High-traffic hour
Low-traffic hour
11
Notes: a new project description

## Slide 13: Scenario with different traffic intensity
    Sequence pressure
High-traffic hour
Low-traffic hour
12
Notes: a new project description

## Slide 14: Scenario with heavy delays
    Minimum time to final
    Heavy delays due to severe snowfall on February 26
13
Notes: a new project description

## Slide 15: Scenario with heavy delays
    Spacing deviation and sequence pressure
    Heavy delays due to severe snowfall on February 26
14
Notes: a new project description

## Slide 16: Study of KPI dynamics
  Heavy delays due to severe snowfall on February 26
15
Notes: a new project description

## Slide 17: Detecting the hotspots with potential separation violations
Orange and green a/c separated by 80 sec, and red and green separated by 159 sec
Purple and blue a/c have already landed. Yellow a/c is at a safe distance
Black and cyan a/c separated by 106 sec, and grey and black a/c separated by 93 sec
16
Notes: a new project description

## Slide 18: Conclusions and future work
  Fine-grained comprehensive assessment of the TMA arrival performance
  Sequence pressure KPI helps to capture the cases of the potential separation violations
  The KPIs can be used to uncover inefficiencies in TMA, allowing the aviation authorities to pinpoint areas where efficiency is lost and suggest directions for the improvements
  Contribution towards the development of multidimensional adaptive KPIs, which will enable creating a comprehensive picture of the operations and faithfully characterizing ATM performance
  Our future work will target the development of new such KPIs capturing other aspects of the TMA performance, as well as testing their applicability for evaluation of the optimization activities within TMA
17
Notes: a new project description

## Slide 19: Thank you!
Notes: a new project description