## Slide 1
Remote Pilotage, Swedish Maritime Administration, DATS 2024
Anders Johannesson

## Slide 2: The plan for this presentation:
A recap of maritime pilotage
Recap of what we have done in the two projects Navigational Support from Ashore (Remote Pilotage) 1 and 2
A couple of beautiful papers
Workload
An exhaustive list
Three simulations
Conclusions
What the conclusions can be used for
Next step

## Slide 3: Recap of Maritime Pilotage. Why Pilot?
Local geographical knowledge
Expertice in ship handling and tugboat handling
Knowledge of port regulations and practices

## Slide 4: Why Remote Pilotage?
Ordinary Pilotage
PEC (Pilot Excemption Certificate)
NSA (Remote Pilotage)

## Slide 5: Suitable Vessels and well prepared crews

## Slide 6
Two differences with our way of Remote Pilotage

## Slide 7: ”Remote Pilotage must be as safe as ordinary pilotage or even safer”

## Slide 8: Workload, three rounds of simulations. First round.
March 24th 2023 – Could the same methods and sensors be used
in maritime remote pilotage context as
previously had been used research about
remote towers?
The Sensors - Video (capturing the NSA Pilot, his screens, all
communications etc.) Pulse Watch, Eye-tracking
glasses and EFT (Electronic Subjective Feedback
Collection Tool) and also Interviews
The scenarios - Two scenarios each 45 minutes long. Quite
demanding.
The results - Worked nice, we could see shifting levels of workload during the
scenarios

## Slide 9: Second round, one NSA-pilot assisting two Vessels simultaneously. Inspired by Remote Tower workload research.

## Slide 10: Second round, first simulation, an example

## Slide 11: The NSA-pilot´s pupil diameter

## Slide 12: Fixations

## Slide 15: What is he thinking about?
IRA HAYES
DONSÖ TURN MEETING IRA HAYES
GODAFOSS CURRENT AND MEETING
BOTH VESSELS TURNING

## Slide 16: Great! Awesome! Super!  But can we use this?

## Slide 17
An exhaustive list:
Eight maritime pilots with NSA-pilotage experience from the simulator were asked to list the (in their opinion) biggest challenges with not being on board while piloting a vessel.
Quite a few bullets that could be sorted in to some five or six groups
Pilotage
I cannot see the conning display…

## Slide 18: Nor can I see this…

## Slide 19: Or this…